## Slide 1: Key and Ultrasonic
許佳興
jiashing@tea.ntue.edu.tw
(視覺與感測技術應用實驗室)
助教: 蔡駿鋼
2021.05.07

## Slide 2: Key

## Slide 3: 按鈕

## Slide 4: Python: global
使用函數內(def)全局變量(global)的例子：
x = 50
def func():
global x
print('x的值是', x)
x = 2
print('全局變量x改為', x)
func()
print('x的值是', x)
--------------------------------------
輸出：
x的值是50
全局變量x改為2
x的值是2

## Slide 5: Python: pass
pass語句是一個空(null)操作;
在程式中使用 pass 語句，執行程式後，你會發現什麼事也沒做，亦即delay一行程式時間

## Slide 6: Threaded callbacks
https://sourceforge.net/p/raspberry-gpio-python/wiki/Inputs/
RPi.GPIO runs a second thread for callback functions. This means that callback functions can be run at the same time as your main program, in immediate response to an edge. For example:
def my_callback(channel):
print('This is a edge event callback function!')
print('Edge detected on channel %s'%channel)
GPIO.add_event_detect(channel, GPIO.RISING, callback=my_callback)

## Slide 7: GPIO.add_event_detect(,,)
GPIO.add_event_detect(KEY, GPIO.RISING, callback=my_callback)
給KEY腳位添加一個事件函數，觸發條件是：捕獲到上升沿（GPIO.RISING）。
GPIO.RISING這個參數還可以是：GPIO.FALLING（下降沿）、GPIO.BOTH（兩者都有）

## Slide 8: GPIO.add_event_detect(,,)
GPIO.add_event_detect(KEY, GPIO.RISING, callback=my_callback, bouncetime=200)
其中bouncetime=200 是延時200ms的意思。就是每間隔200ms才會執行這個中斷裡面的程序。
可以避免機器開關彈跳的現象

## Slide 9: 機器開關彈跳的現象

## Slide 10
import RPi.GPIO as GPIO
import time
GPIO.setmode(GPIO.BCM)
# Key connect to GPIO2
# LED connect to GPIO18
LED = 18
KEY = 2
GPIO.setup(KEY, GPIO.IN, GPIO.PUD_UP)
GPIO.setup(LED, GPIO.OUT)
ledStatus = True
def my_callback(channel):
print("button pressed!")
global ledStatus
ledStatus = not ledStatus
if ledStatus:
GPIO.output(LED, GPIO.HIGH)
pass
else:
GPIO.output(LED, GPIO.LOW)
pass
pass

## Slide 11
#GPIO.add_event_detect(KEY, GPIO.RISING, callback=my_callback)
#GPIO.add_event_detect(KEY, GPIO.FALLING, callback=my_callback)
#GPIO.add_event_detect(KEY, GPIO.RISING, callback=my_callback, bouncetime=200)
GPIO.add_event_detect(KEY, GPIO.FALLING, callback=my_callback, bouncetime=200)
while True:
try:
print("I'm working...")
time.sleep(5)
pass
except KeyboardInterrupt:
break
pass
pass
GPIO.cleanup()

## Slide 12: 機器開關彈跳應變: 方法2
try:
while True:
if GPIO.input(BtnPin) == True:
time.sleep(0.01)
if GPIO.input(BtnPin)==True:
GPIO.output(Rpin,1)
GPIO.output(Gpin,0)
elif GPIO.input(BtnPin) == False:
time.sleep(0.01)
if GPIO.input(BtnPin) == False:
while GPIO.input(BtnPin) ==True:
pass
GPIO.output(Rpin,0)
GPIO.output(Gpin,1)
except KeyboardInterrupt: # When 'Ctrl+C' is pressed, the child program destroy() will be executed.
GPIO.cleanup()

## Slide 13: 超音波 Ultrosonic
Raspberry Pi：超音波測距離

## Slide 14: 基礎知識：超音波測距
超音波測距的方式是發射一個電波，當電波遇到物體反射回來，再被測距儀偵測到反射電波，利用來回時間與音波的速度算出距離，計算公式如下：
距離=(音波發射與接收時間差 * 聲音速度(340 m/s))/2
聲音的速度，在一般空氣中約為每秒340公尺，因來回時間要將距離除以二，才是單程的距離。實際的聲音速度決定於好幾個環境因素，其中一個是溫度，計算時，需將環境因素考慮在內，才能更精確計算距離。

## Slide 15: 基礎知識：超音波測距
超音波測距的方式是發射一個電波，當電波遇到物體反射回來，再被測距儀偵測到反射電波，利用來回時間與音波的速度算出距離，計算公式如下：
距離=(音波發射與接收時間差 * 聲音速度(340 m/s))/2
聲音的速度，在一般空氣中約為每秒340公尺，因來回時間要將距離除以二，才是單程的距離。實際的聲音速度決定於好幾個環境因素，其中一個是溫度，計算時，需將環境因素考慮在內，才能更精確計算距離。

## Slide 16: 常見的超音波模組

## Slide 17: 常見的超音波模組
• VCC：接電源（範圍2.4V~5.5V）。 • Trig/TX：UART 模式下，接外部電路UART 的TX 端；為GPIO模式時，為訊號發送端 Trigger。 • Echo/RX：UART 模式下，接外部電路UART 的RX 端；為GPIO模式時，為訊號接收端 Echo 。 • GND：接地，沒有使用。 • GND：電路接地。 工作方式： 透過Trig接腳發出一個10us（10^-5秒）以上的高電位，此時等待Echo高電平輸出，一旦有輸出就可以開始計時，此時模組會發送8個40khz的方波，並開始自動檢測是否有返回信號；當偵測到反射訊號時，此時Echo接腳變為低電位。計算持續高電位的時間，也就是這次測距的時間。如果加上迴圈，就可以一直偵測前方移動物體的距離。

## Slide 18: 工作方式

## Slide 19: 工作方式
透過Trig接腳發出一個10us（10^-6 秒）以上的高電位，此時等待Echo高電平輸出，一旦有輸出就可以開始計時，此時模組會發送8個40khz的方波，並開始自動檢測是否有返回信號；當偵測到反射訊號時，此時Echo接腳變為低電位。計算持續高電位的時間，也就是這次測距的時間。如果加上迴圈，就可以一直偵測前方移動物體的距離。

## Slide 20: 工作方式
超音波測距 ，使用 HC-SR04 模組，這個模組包括超音波發送器、超音波接收器和控制電路如下圖，測距範圍從 2 公分至 400公分(4 公尺)，精密度0.3公分。
Vcc 接5V
Trig 觸發 (輸入脈波至少10us)
Echo 檢測接收回音信號(接收後輸出高準位電壓)
Gnd 接地

## Slide 21: 工作方式
超音波測距的方式是發射一個電波，當電波遇到物體反射回來，再被測距儀偵測到反射電波，利用來回時間與音波的速度算出距離，計算公式如下：
距離 = (音波發射與接收時間差 * 聲音速度 (340M/S) ) / 2

## Slide 22: 工作方式
啟動樹莓派發出至少10us 的觸發脈波到 HC-SR04 模組的trig腳，使得 HC-SR04 模組產生8個40KHz(25us)超音波的脈波，接著樹莓派由零開時計時，HC-SR04 模組的Echo腳 變為高準位，等待接收回音信號，Echo腳準位降低時，樹莓派把計時值轉變為距離。
每58.3us的時間為1公分，回音越久接收，Echo腳高準位時間越久，距離越遠。
檢測距離=(40KHz(25us)超音波的脈波的傳送速度X 檢測時間)/2
=(343公尺/秒X檢測時間秒數)/2
1s-->171.5m ;
1ms-->171.5mm=17.15cm
17.15公分約1ms
1公分約 58.3us
註：
1. 音速約340公尺/秒，參考http://www.phy.ntnu.edu.tw/demolab/html.php?html=modules/sound/section1
2. 因為來回時間，所以除以2

## Slide 23: 線路連接與電路圖 https://sites.google.com/site/rasberrypintust/shu-mei-pai-xiao-ji-qiao/8-hc-sr04-chao-yin-bo-gan-ce-qi
Vcc 接 pin2 (+5V)
GND 接 pin6 (GND)
Trig 接 Pin16 (GPIO23)
Echo 接 Pin18 (GPIO24)

## Slide 24: 程式 1
import time
import RPi.GPIO as GPIO
GPIO.setmode(GPIO.BCM)
# Define GPIO to use on Pi
GPIO_TRIGGER = 23
GPIO_ECHO = 24
print ("Ultrasonic Measurement“)
# Set pins as output and input
GPIO.setup(GPIO_TRIGGER,GPIO.OUT) # Trigger
GPIO.setup(GPIO_ECHO,GPIO.IN) # Echo
# Set trigger to False (Low)
GPIO.output(GPIO_TRIGGER, False)
time.sleep(0.5)

## Slide 25: 程式 1
# Send 10us pulse to trigger
GPIO.output(GPIO_TRIGGER, True)
time.sleep(0.00001)
GPIO.output(GPIO_TRIGGER, False)
start = time.time()
while GPIO.input(GPIO_ECHO)==0:
start = time.time()
while GPIO.input(GPIO_ECHO)==1:
stop = time.time()
# Calculate pulse length
elapsed = stop-start
# Distance pulse travelled in that time is time
# multiplied by the speed of sound (cm/s)
distance = elapsed * 34000
# That was the distance there and back so halve the value
distance = distance / 2
print("Distance : %.1f" % distance)
# Reset GPIO settings
GPIO.cleanup()

## Slide 26: 程式 2
import RPi.GPIO as GPIO
import time
trigger_pin = 23
echo_pin = 24
GPIO.setmode(GPIO.BCM)
GPIO.setup(trigger_pin, GPIO.OUT)
GPIO.setup(echo_pin, GPIO.IN)
def send_trigger_pulse():
GPIO.output(trigger_pin, True)
time.sleep(0.001)
GPIO.output(trigger_pin, False)
def wait_for_echo(value, timeout):
count = timeout
while GPIO.input(echo_pin) != value and count > 0:
count = count - 1

## Slide 27: 程式 2
def get_distance():
send_trigger_pulse()
wait_for_echo(True, 5000)
start = time.time()
wait_for_echo(False, 5000)
finish = time.time()
pulse_len = finish - start
distance_cm = pulse_len * 340 *100 /2
distance_in = distance_cm / 2.5
return (distance_cm, distance_in)
while True:
print(“cm=%f\t inches=%f" % get_distance())
time.sleep(1)

## Slide 28: Q&A